## Slide 1: NT 21

## Slide 2: Week 1 : Introduction (Networks, Layered Model, Linux) Week 2 : IP Protocol, IP Addressing, IP Subnets , ARP, Netkit Week 3 : IP Routing, ICMP Week 4 : TCP/UDP Week 5 : Sockets Week 6 : NAT, DHCP, DNS Week 7 : Repetition
Program

## Slide 3: Layered Communication: TCP/IP Protocols Overview
Physical Layer
DataLink Layer
Network Layer
Transport Layer
Application Layer
HTTP
DHCP
FTP
DNS
DHCP
Telnet
SMTP
TCP
UDP
IP
Ethernet
Wifi
Bluetooth
Bluetooth
Wifi
Ethernet

## Slide 4: TCP/UDP
TCP and UDP are two most used transport layer protocols. TCP and UDP provide peer-to-peer communication for the application processes.

## Slide 5: TCP/UDP Transport Layer
email
web
browser
email
web
server
streaming
client
streaming
server
…
…
Host-to-Host Communication (IP protocol)
Application Process-to-Application Process Communication (TCP/UDP protocol)
192.168.1.1
173.12.122.1
25
143
1340
80
6430
554

## Slide 6: TCP/UDP TCP/UDP ports
Port addresses specify source and destination application process and are represented by a 16 bit unsigned number.
Well-known ports
0-1023
Registered ports
Dynamic/private ports
1024-49151
>49151
e.g. 21 for FTP, 80 for HTTP,
53 for DNS, …
Assigned by Internet Assigned
Number Authority
for vendors
Often dynamically (on demand)
Allocated for the source port
(ephemeral ports)

## Slide 7: UDP User Datagram Protocol (UDP)
connection-less
error control with checksums optional
works with datagrams
unreliable
simple to implement
fast

## Slide 8: TCP Transmission Control Protocol (TCP)
connection-oriented
flow control
congestion control
error control
works with segments
stream-oriented
reliable
full-duplex

## Slide 9: TCP TCP: Connection-oriented
1. Phase
Connection Establishment
(3 way handshake)
2. Phase
Data Transfer
3. Phase
Connection Tear-Down
(3 way handshake)
SYN
ACK
SYN+ACK
DATA+ACK
DATA+ACK
DATA+ACK
DATA+ACK
FIN
ACK
FIN+ACK
SERVER
CLIENT

## Slide 10: TCP Flow Control
TCP Connection
Hello !
How fast can I
send data ?
I’m busy now.
Send data
slowly

## Slide 11: TCP Flow Control
Sequence Numbers – keep track of how much data is sent. It is included in
every TCP packet. The sequence number represents the first byte number in the
TCP byte stream being sent to the receiver.
Acknowledgement Numbers – keep track of how much data was successfully
received. It is included in TCP packets when the sender’s data is being
acknowledged. The acknowledgment number represents the next byte in the TCP
byte stream the receiver is expecting.
Sliding Window Protocol – a protocol that keeps track of number of data being
sent, the number of data already acknowledged and how much data the receiver
can buffer before sending the data to the application (receive window).

## Slide 12: TCP/UDP TCP Sliding Window Example
RECEIVER
SENDER
Application
sends 2048
bytes of data
Empty
Receiver’s buffer
size 4096
Seq=0
2048
2048
Ack=2048 WinSize=2048
Application
sends next 2048
bytes of data
Seq=2048
2048
Full
Ack=4096 WinSize=0
2048
Ack=4096 WinSize=2048
Seq=4096
1024
2048
1024
Application
processes 2048 bytes
Application
is blocked

## Slide 13: TCP Error Control
Checksum – used to detect corrupted data
Retransmissions – lost and corrupted data are retransmitted
Sequence/acknowledgment numbers, acknowledgments and sliding window
protocol are also used for error control

## Slide 14: TCP Error Control Examples (1)
DATA
Data gets corrupted
during transfer
Data is dropped
by the receiver
Timeout
DATA
Data is
retransmitted
ACK

## Slide 15: TCP Error Control Examples (2)
DATA
Packet lost during transfer
Timeout
DATA
Data is
retransmitted
ACK

## Slide 16: TCP Error Control Examples (3)
DATA
Acknowledgement lost
Timeout
DATA
Data is
retransmitted,
duplicate packets
ACK
ACK

## Slide 17: TCP Error Control Examples (4)
DATA
Early Timeout
Timeout
Data is
retransmitted,
duplicate packets
ACK
ACK
DATA